ABTEC-WI099-A0

A2產品技術規格書

| 產品型號 | ABTEC-A2 |
| --- | --- |
| 產品功能 | 音訊測試分析儀 |
| 產品版本 | V1.0 |
| 產品外觀 | 前面板圖 |  |
|  | 後面板圖 |  |

2014.03.22

| 目錄TABLE OF CONTENTS |
| --- |
| 序號 NO. | 項目 ITEM | 頁碼 PAGE |
|  | 目錄 | 1 |
| 1 | 適用範圍 | 2 |
| 2 | 一般規範 | 2 |
| 3 | 功能模組 | 2 |
| 4 | 性能參數 | 3-9 |
| 5 | BT選件 | 10-11 |
| 6 | WIFI選件 | 12 |
| 7 | HDMI選件 | 13 |
| 8 | ACO選件 | 14 |
| 9 | 語音選件 | 15 |
| 10 | 環境試驗特性 | 16 |
| 11 | EMC特性 | 17 |
| 12 | 產品遵守標準(國際標準/國家標準/行業標準/企業標準) | 17 |

一．適用範圍

本產品適用於音訊電路板及音訊終端設備的測試應用。

二．一般規範

| 序號 | 專案參數 | 規格要求 |
| --- | --- | --- |
| 2.1 | 外形尺寸 | 428mm*318mm*120mm |
| 2.2 | 重量 | 5kg±0.5kg |
| 2.4 | 工作溫度 | 0℃ ~ 45℃ |
| 2.5 | 貯存溫度 | -40ºC~75ºC |
| 2.6 | 濕度 | 10~80% |

- 功能模組

| 模擬輸出通道數： | 2通道 |
| --- | --- |
| 模擬輸入通道數： | 2通道 |
| 數位輸出通道數： | 1通道 |
| 數位輸入通道數： | 1通道 |
| 模擬輸出埠類型： | XLR/BNC |
| 模擬輸入埠類型： | XLR/BNC |
| 數位輸出埠類型： | XLR/BNC/OPT |
| 數位輸入埠類型： | XLR/BNC/OPT |
| 音視頻輸入埠類型: | AUX IN/OUT |
| 通訊埠類型： | USB/串口 |

四．性能參數

| Characteristic | Specifications | Supplemental Information |
| --- | --- | --- |
| ANALOG GENERATOR |
| Number of Channels | 2, independent amplitude control |  |
| Waveforms | Sine, sine split frequency, sine split phase, sine+DC offset, continuously swept-sine, noise, IMD test signals, multi-tone, wave file playback |  |
| Sine Characteristics |
| Frequency Range (Fs) | 2 Hz to 80.1 kHz | Setting resolution is typically 45 µHz |
| Frequency Accuracy | ±(0.0003% + 100 μHz) |  |
| Amplitude Range | 0 to 16.00 Vrms [45.2 Vpp], balanced; 0 to 8.00 Vrms [22.6 Vpp], unbalanced |  |
| Amplitude Accuracy, 1 kHz | ±0.05 dB [±0.58%] |  |
| Flatness (1 kHz ref) |  |  |
| Fs = 10 Hz to 20 kHz | ±0.010 dB | typically <0.005 dB. |
| Fs = 20 kHz to 50 kHz | ±0.030 dB |  |
| Fs = 50 kHz to 80 kHz | ±0.10 dB |  |
| Residual THD+N |  |  |
| Fs = 20 Hz–20 kHz | ≤ (–102 dB + 1.4 µV), 20 kHz BW |  |
| Non-Harmonic Content |  | Typically <-110 dB when Fs ≤75 kHz, increasing to ≈-55 dB at Fs =80 kHz |
| Phase Offset Range (SplitPhase) | –179.999 to +180.000 deg |  |
| DC Offset Range | ±12.00 Vdc balanced; ±6.00 Vdc unbalanced | DC offset limits maximum ac signal |
| Residual DC Offset | ≤0.25% of Vrms setting [≤0.09% of Vpp setting] + 100 μV |  |
| Characteristic | Specifications | Supplemental Information |
| Noise Characteristics |
| Shape | White (<5 Hz to 86.4 kHz), Pink (<10 Hz to 86.4 kHz), IEC 60268-1 or BS EN 50332-1 |  |
| Amplitude Range | 0 to 45.2 Vpp, balanced; 0 to 22.6 Vpp, unbalanced | Amplitude calibration is approximate |
| IMD Test Signals (requires option AML) |
| SMPTE & MOD |
| Lower Frequency (LF) | 40 Hz to 1.00 kHz |  |
| Upper Frequency (HF) | 2.00 kHz to 60.00 kHz | HF tone must be≥6 • LF tone. |
| Mix Ratio (LF:HF) | 10:1, 4:1 or 1:1 | 4:1 maximum with SMPTE signal. |
| Amplitude Range | 0 to 45.2 Vpp, balanced; 0 to 22.6 Vpp, unbalanced. |  |
| Amplitude Accuracy | ±0.06 dB [±0.70%] |  |
| Residual IMD | ≤0.0025% [-92 dB], 4:1 mix ratio |  |
| DFD |
| Difference Frequency (Fdiff) | 80 Hz to 2.00 kHz | Fmean = (F1 + F2)/2. |
| Mean Frequency (Fmean) | 250 Hz to 60.00 kHz | Fdiff = ¦F2 - F1¦ Fmean Must be ≥6 • F diff |
| Amplitude Range | 0 to 45.2 Vpp, balanced; 0 to 22.6 Vpp, unbalanced. |  |
| Amplitude Accuracy | ±0.06 dB [±0.70%] |  |
| Residual IMD | ≤0.0010% [–100 dB] |  |
| Multitone, Wave File Playback (requires option HST) |
| Sample Rate Range (SR) | 8 kS/s to 108 kS/s, and 175 kS/s to 192 kS/s | Operation from 109 kS/s to 175 kS/s is possible, but with degraded flatness |
| Maximum File Size | 32 MSample. |  |
| Amplitude Range | 0 to 45.2 Vpp, balanced; 0 to 22.6 Vpp, unbalanced. | .Wav file must peak at digital full scale to obtain selected amplitude |
| Characteristic | Specifications | Supplemental Information |
| Flatness (1 kHz ref) |  |  |
| SR = 175 kS/s to 192 kS/sec |  | Typically <0.012 dB to 20 kHz |
| SR = 8 kS/s to 108 kS/s |  | Typically <0.04 dB to 20 kHz; max frequency limited to ≈0.45 • SR |
| Spurious Content |  | Typically <–100 dB |
| Output Equalization | Arbitrary 30-pole output filter |  |
| Source Resistance (Rs) |
| Balanced | Selectable 100 Ω±1% or 600Ω±1%. | Grounded, symmetrical |
| Unbalanced | Selectable 50Ω±1.5% or 600Ω±1%. |  |
| Common Mode Test | Same as Balanced selections |  |
| Max Output Current |  | Typically >50 mA peak, 50 mA dc |
| Reverse Overload Protection |  | Up to 30 W |
| Output Related Crosstalk | ≤(–120 dB + 1 µV) to 20 kHz |  |
| ANALOG ANALYZER |
| Number of Channels | 2, independently auto-ranging. | Max ADC sample rate = 192 kS/s |
| Maximum Rated Input | 230 Vpk, 230 Vdc any input to ground; |  |
| Input Impedance |
| Balanced | 100 kΩ¦¦ ≈230 pF, each side to gnd |  |
| Unbalanced | 100 kΩ¦¦ ≈230 pF to bnc shield |  |
| Input Termination | Selectable 600Ω±1%, 1.5 W max. | Termination automatically opens in the 80 V range. |
| Characteristic | Specifications | Supplemental Information |
| Input Coupling | Selectable DC or AC | Typically <0.5 μA bias current with DC coupling, typically <0.03 dB roll-off at 20 Hz with AC coupling |
| Input Ranges | 250 mVrms to 250 Vrms | Maximum ac signal is ≈230 Vac unbal, 350 Vac bal, in the 250V range |
| Common Mode Rejection |  | Max common mode signal range: |
| 250 mV, 800 mV, 2.5 V ranges | ≥80 dB, 5 Hz to 5 kHz; ≥70 dB, 5 kHz to 20 kHz. | ±6 Vpk |
| 8 V range | ≥50 dB, 5 Hz to 20 kHz | ±12 Vpk |
| 25 V range | ≥50 dB, 5 Hz to 20 kHz | ±60 Vpk |
| 80 V range | ≥45 dB, 5 Hz to 20 kHz | ±120 Vpk |
| 250V range | ≥45 dB, 5 Hz to 20 kHz | ±230 Vpk |
| Input Related Crosstalk | ≤(–120 dB + 0.3 µV) to 20 kHz | Rs≤600Ω |
| Level (Amplitude) Measurement |
| Range |  |  |
| Balanced or bridging input | < 1 µV to 350 Vrms |  |
| Unbalanced input | < 1 µV to 230 Vrms |  |
| Accuracy (1 kHz) | ±0.05 dB [±0.60%] |  |
| Flatness (1 kHz ref, DC coupling) |  |  |
| 10 Hz to 20 kHz | ±0.010 dB | Typically < 0.005 dB. |
| 20 kHz to 50 kHz | ±0.030 dB |  |
| 50 kHz to 80 kHz | ±0.10 dB |  |
| Residual Noise (inputs shorted) | ≤ 1.4 µVrms, 20 kHz BW | Typically < 8.0 nV/√Hz at 1 kHz |
| THD+N Measurement |
| Fundamental Range | 5 Hz to > 90 kHz |  |
| Measurement Range | 0 to 100% |  |
| Accuracy | ±0.5 dB |  |
| Residual THD+N |  |  |
| 20 Hz–20 kHz fundamentals | ≤(–102 dB + 1.4 µV), 20 kHz BW |  |
| Bandwidth Limiting Filters |
| High-Pass |  |  |
| Characteristic | Specifications | Supplemental Information |
| DC | DC coupling |  |
| AC (< 10 Hz) | AC coupling | Response is 2-pole via a combination of analog and digital filters, and is typically –3 dB at 4.1 Hz |
| Butter worth | FHP (–3 dB) = 10 Hz to 90 kHz, 4-pole |  |
| Elliptic | FHP (–0.01 dB) = 10 Hz to 90 kHz; 5-pole; 0.01 dB pass-band ripple; ≤–60 dB stop-band |  |
| Low-Pass |  |  |
| ADC Pass band | No filter is implemented, bandwidth and response are limited by the A/D and sample rate (SR) | –3 dB at ≈ 0.490 • SR, SR ≤216 kS/s |
| 20k (AES17), 40k (AES17) | Special filters conforming with AES17 |  |
| Butterworth | FLP (–3 dB) = 10 Hz to 90 kHz, 8-pole | ENBW ≈ 1.006 • FLP |
| Elliptic | FLP (–0.01 dB) = 10 Hz to 90 kHz, 8-pole; 0.01 dB pass-band ripple; ≤–60 dB stop-band | ENBW ≈ (1.012–1.062) • FLP (varies due to warping) |
| Weighting | A-wt,B-wt,C-wt,CCIR-1k,CCIR-2k,CCITT,C-message,50μs or 75μs de-emph(with and without A-wt),or None | Weighting filter is cascaded with both high-pass and low-pass filters |
| Input Equalization | Arbitrary 30-pole input filter | The EQ operates on any selected analyzer input channels. |
| Characteristic | Specifications | Supplemental Information |
| IMD Measurement |
| Test Signal Compatibility |  |  |
| SMPTE & MOD | Any combination of 40 Hz–1 kHz (LF) and 1kHz–60kHz (HF), mixed in any ratio from 1:1 to 10:1 (LF:HF) | HF tone must be≥6•LF tone. |
| DFD | Any two-tone combination with mean frequency of 250 kHz–60 kHz and a difference frequency of 80 Hz–2.0 kHz | Fmean = (F1+F2)/2, Fdiff = ¦F2–F1¦. Fmean must be≥6•Fdiff |
| IMD Measured |  |  |
| SMPTE | Amplitude modulation of HF tone. | Measurement BW is typ. 40–750 Hz. |
| MOD | d2, d3, d2+d3, or d2+d3+d4+d5 | Use“d2+d3”for measurements per IEC 60268 |
| DFD | d2, d3, d2+d3, or d2+d3+d4+d5 | Use“d2+d3”for measurements per IEC 60268 |
| Measurement Range | 0 to 20% |  |
| Accuracy | ±0.5dB |  |
| Residual IMD |  |  |
| SMPTE & MOD | ≤-92 dB [0.0025%], 4:1 mix ratio |  |
| DFD | ≤-100 dB [0.0010%] |  |
| Frequency Measurement |
| Range | 5 Hz to 90 kHz |  |
| Accuracy | ±0.0003% [3 ppm] | Vin must be ≥ 5 mV. |
| Resolution | 6 digits |  |
| Phase Measurement |
| Ranges | –90 to +270, ±180, or 0 to 360 deg |  |
| Accuracy | ±0.2 deg, 5 Hz to 5 kHz; ±0.8 deg, 5 kHz to 20 kHz; ±2.0 deg, 20 kHz to 50 kHz | Vin must be ≥ 5 mV with dc coupling,both channels. Accuracy degrades below 50 Hz with ac coupling. |
| Resolution | 0.001 deg |  |
| DC Voltage Measurement |
| Input Ranges | 0.25 V to 250 V | ±230 Vdc maximum in 250V range |
| Characteristic | Specifications | Supplemental Information |
| Accuracy |  |  |
| 250 mV and 800 mV ranges | ±(0.7% reading + 1 mV) |  |
| 2.5 V-250 V ranges | ±(0.7% reading + 0.1% range) |  |
| Normal Mode Rejection |  | Typically > 90 dB, 20 Hz to 20 kHz. |
| DIGITAL I/O |
| DIGITAL OUTPUT RELATED: |
| Formats |  |  |
| Electrical, unbalanced | SPDIF-EIAJ per IEC60958, 0.50 Vpp or 1.00 Vpp ±10% into 75Ω | Output R is nominally 75Ω. |
| Electrical, balanced | AES-EBU per AES3-1992, 5.00 Vpp ±10% into 110Ω | Output R is nominally 110Ω. |
| Optical | Toslink |  |
| Sample Rate (SR) Range |  |  |
| Electrical | 27 kS/s to 200 kS/s | Usable over the extended range of 16 kS/s to 216 kS/s with degraded waveform |
| Optical | 27 kS/s to 108 kS/s |  |
| Sample Rate (SR) Accuracy | ±0.0003% [3 ppm] |  |
| Channel Status Bits | Full implementation per IEC-60958 | Automatically set or manual override, hex or plain English |
| User Bits and Validity Flag | Fully settable |  |
| Electrical |  | Typically < 1.5 ns |
| Optical |  | Typically < 2.5 ns, SR ≤ 96 kS/s |
| EMBEDDED OUTPUT SIGNAL RELATED: |

- AX- BT 選件

BT/WIFI 埠

5.1AX- BT - RD 選件

| 5.1.1 | 藍牙協議版本 | 2.1+EDR |
| --- | --- | --- |
| 5.1.2 | Profiles/Roles Supported | A2DP Source |
|  |  | A2DP Sink |
|  |  | HFP Audio Gateway |
|  |  | HFP Hands-Free |
|  |  | HSP Audio Gateway |
|  |  | HSP Headset |
|  |  | AVRCP Controller |
| 5.1.3 | Codecs Supported | SBC |
|  |  | APT-X |
| 5.1.4 | RF埠類型 | Type N, Female |
|  |  | BT Antenna (2.4GHz) |
| 5.1.5 | RF 輸入阻抗 | 50 Ω |
| 5.1.6 | RF 輸出阻抗 | 50 Ω |
| 5.1.7 | RF 功率 | 0 dBm;最大可以達到 +4 dBm |
| 5.1.8 | RF 靈敏度(0.1% BER) | –81 dBm |

5.2 AX- BT - PT 選件

從搜索-配對-連接 時間較短 約為5秒.

| 5.2.1 | 藍牙協議版本 | 2.1+EDR |
| --- | --- | --- |
| 5.2.2 | Profiles/Roles Supported | A2DP Source |
|  |  | HFP Hands-Free |
|  |  | AVRCP Controller |
| 5.2.3 | Codecs Supported | SBC |
|  |  | APT-X |
| 5.2.4 | RF埠類型 | Type N, Female |
|  |  | BT Antenna (2.4GHz) |
| 5.2.5 | RF 輸入阻抗 | 50 Ω |
| 5.2.6 | RF 輸出阻抗 | 50 Ω |
| 5.2.7 | RF 功率 | 0 dBm;最大可以達到 +4 dBm |
| 5.2.8 | RF 靈敏度(0.1% BER) | –81 dBm |

- AX- WIFI

| 6.1 | 無線通訊標準 | WIFI 802.11 a/b/g/n Dual Band Ratio |
| --- | --- | --- |
| 6.2 | APP 控制協議 | DLNA |
|  |  | AirPlay |
|  |  | QPlay |
| 6.3 | 頻率範圍 | 2.412-2.484GHz |
| 6.4 | 傳輸功率（Typical） | 17dBm(802.11b DSSS) |
|  |  | 17dBm(802.11b CCK ) |
|  |  | 15dBm(802.11q/n OFDM) |
| 6.5 | 接受靈敏度（Typical） | -71.0dBm(<10%PER)@65Mbps |
|  |  | -74.0dBm(<10%PER)@54Mbps; |
|  |  | -94.0dBm(<10%PER)@1Mbps; |
| 6.6 | RF埠類型 | Type N, Female |
|  |  | N- SMA Antenna (2.4GHz) |
| 6.7 | RF 輸入阻抗 | 50 Ω |
| 6.8 | RF 輸出阻抗 | 50 Ω |

七. AX- HDMI

AX- HDMI選件（HDMI+音訊回傳通道（ARC）是一種多功能的音訊監視和音訊測量的功能選件,它功能強大，使用簡單方便,測量結果準確，可廣泛應用於多媒體產品的音訊品質測試，可提供的所有標準音頻測量值包括電平、信噪比（SNR）、失真、相位、串音、群延遲等。

HDMI 介面

主要功能：

執行標準：HDMI1.4；

介面類別型：type A；

通道數：2，8

比特：8bit 到24bit

取樣速率：可達192kHz

支援格式：PCM、Dolby Digital、DTS等

具有支援接收器和電視的ARC音訊品質和可連線性的功能；

具有生成線性/PCM音訊流，支援從編碼前的音訊測試檔中生成無損格式

(比如杜比TrueHD™和dts-HD主音訊™)和壓縮格式（比如杜比數位™和dts數位環繞身歷聲™)；

具有相容性和減採樣/縮混/轉碼功能；

支援高清晰度多媒體介面音訊回傳通道；

具有查看和編輯HDMI 增強擴展顯示識別資料(E-EDID)；

支援多個EDID配置；

具有生成視訊訊號（解析度達到1080P)和協力廠商視頻支援。

- 電聲選件 AX- ACO

A2揚聲器研發/生產測試選件，以單次快速掃描和易用性提供多參數檢查揚聲器的規格和性能，確保揚聲器和音箱的完整性，並同時檢查Rub & Buzz 缺陷、相對電平、相位、失真比和失真雜訊電平等，比較黃金樣本 。

通過快速連續掃描信號，找出高振幅因數和高峰值比從而檢查 Rub & Buzz 異音缺陷。這些缺陷包括音圈移位、鬆散在音圈隙、不完全粘連的懸浮物料等；在這些情況下，所產生的問題是瞬變和很難檢測到，不能使用標準計算例如 FFT測量或人工檢測。

主要功能:

☆基本電聲參數測量 （阻抗和 T/S小參數 ）

☆SPL/THD測試

☆喇叭生產測試

☆異音Rub & Buzz 檢測

☆瀑布和極化圖

☆空氣洩露檢測

☆其他聲學測量

九. 主觀音質評測選件

AX-PESQ     基於ITU-T P.862標準

AX-POLQA2   基於 ITU-T P.863標準

感知音訊測量廣泛應用與智慧手機，VoIP 網路和設備測試，衡量人們如何感知聲音品質。感知聲音品質測試是特別有用於寬頻或位元元速率有限的設備，使用標準的正弦波測試如頻響和失真等這些參數不能有效地測試和比較不同設備性能；最後，只有用感知和電氣音訊測試組合，才可以完全説明這些設備的性能。

PESQ是一個感知語音品質測量工具。它由德國OPTICOM 有限公司開發，根據 ITU-T 建議專為低頻寬的設備，例如手機和智慧手機上測試語音品質，適當的測試信號可以達到類似使用人類測試的結果，有很高的相關性；

POLQA2 加強至寬頻語音品質和聲學介面等等測試。

十. 環境試驗特性

環境試驗特性

| 試驗條件 | 環境溫度 | 15℃～35℃ |
| --- | --- | --- |
|  | 相對濕度 | 25%～75% |
|  | 氣壓 | 86~106kpa |
| 6.1 | 電源適應性 | 執行 GB/T 6587-2012 條款4.10 |
| 6.2 | 介電常數 | 執行 GB/T 6587-2012條款5.8.2 |
| 6.3 | 保護接地 | 執行 GB/T 6587-2012條款5.8.3 |
| 6.4 | 溫度實驗 | 執行 GB/T 6587-2012條款5.9.1 |
| 6.5 | 濕度實驗 | 執行 GB/T 6587-2012條款5.9.2 |
| 6.6 | 衝擊實驗 | 執行 GB/T 6587-2012條款5.9.4 |
| 6.7 | 裸機振動試驗 | 執行 GB/T 6587-2012條款5.9.3 |
| 6.8 | 包裝振動實驗 | 執行 GB/T 6587-2012條款5.10.1 |

十一．EMC 特性

執行 GB/T 6587-2012 《電子測量儀器通用規範》---4.9條款

| 7.1 | 傳導騷擾 | 150kHz～30MHz電源端子的傳導騷擾電壓限值（B級） |
| --- | --- | --- |
| 7.2 | 輻射騷擾 | 輻射騷擾限值 B級 |
| 7.3 | 靜電放電抗擾度 | 性能判據：等級B |
| 7.4 | 射頻電磁場輻射抗擾度 | 性能判據：等級A |
| 7.5 | 電快速瞬變脈衝群抗擾度 | 實驗判據：等級B (GB/T 17626.4-2008 等級四) |
| 7.6 | 浪湧（衝擊）抗擾度 | 實驗判據：等級B |
| 7.7 | 射頻場感應的傳導騷擾抗擾度 | 性能判據：等級A |
| 7.8 | 電壓跌落、暫降和短時中斷抗擾度 | 性能判據：等級B |

十二．產品遵守標準(國際標準/行業標準/企業標準)

本產品遵守如下國家標準：

8.1《GB_T 6587-2012_5625電子測量儀器通用規範》

8.2《JJF 1395-2013 音訊分析儀校準規範》